## Slide 1: WOW
Notes: wowowow

## Slide 2: Finally, Computer Architecture!
01
Notes: Thank you for studying

## Slide 3: Computer Architecture!
Notes: this very challenging hardware course with me.
First, let me ask you some questions. Which hardware courses did you complete?
What did you learn in those courses?
How about software courses?
It’s great to know that you have already built a solid background of computer science.
But as you may or may not have noticed, when you learn the software courses, you follow a top-down approach

## Slide 4: Computer Architecture!
program
Notes: At first, you started with various programming languages, like C and Java.
Through those courses, you might have developed some fancy programs/applications and become very much amazed by how awesome our computers can be.
And hopefully, you might’ve also accumulated a strong interest in computer science.
After a while, you might have become more curious about how exactly your programs are handled by computers.
For example, when you open a file or print a string on the screen, you simply call a function like OpenFile and Print, but you don’t need to worry about how to implement the called functions.
Instead, standard libraries of the programming language in use do that for you.
Meanwhile, you may have noticed that when you install certain sdk on your computer, you usually need to choose a specific version that suits your operating system.

## Slide 5: Computer Architecture!
program
operating system
Notes: So, operating system is a special program that manages other programs.
First, an operating system provides necessary support for function implementation in Libraries. For example, the OpenFile function implementation in Library may further call a function defined in the code of the operating system.
More importantly, an operating system manages computer hardware and software resources and provides common services for computer programs. For example, many tasks may be running on our computers. It is the operating system that decides which task accesses which resources at which time instance.

## Slide 6: Computer Architecture!
program
operating system
digital logic
Notes: When you study the hardware courses, you followed a bottom up approach.
You probably started with Digital Logic, which models computer computation at a very low level.
For example, how information is modeled by signals in a binary fashion, how a single transistor represents a bit, how a gate achieves simple operations over a combination of transistors;

## Slide 7: Computer Architecture!
program
organization
digital logic
operating system
Notes: apparently, it is challenging to always break up a complex computation into sub-computations supported by digital logic
That’s why you get to know more computation units in the course of computer organization.
In computer organization, you also learned other components like CPU, memory, and I/O, that are indispensible for computation.
So far, there is still one major question left unresolved: how exactly do these computer components cooperate to complete a computation?

## Slide 8: Computer Architecture!
operating system
program
organization
digital logic
Notes: In the course of Computer Architecture, you will reveal this missing piece.
As shown in the slide, computer architecture is a layer between software and hardware
It is an Architect/microarchitect’s view of how to design a computer that meets system design goals;
Design choices critically affect both the software programmer and the hardware designer.
So far, any questions?

## Slide 9: Computer Architecture!
?
Notes: What will be covered in this course?
To answer this question, let’s walk through how our computers solve a problem and see where computer architecture fits in.

## Slide 10
problem
electrons
Notes: Given a problem, eventually it’ll be the electrons that drive our computers to generate the result.
But before that, we need to go through a sequence of steps.

## Slide 11
problem
electrons
algorithm
Notes: First, we need to design a method to solve the problem. In computer science, such methods are called algorithms.

## Slide 12
problem
electrons
algorithm
program
Notes: Then based on your algorithm design, you use certain programming language to implement it into an executable program.

## Slide 13
problem
electrons
algorithm
program
runtime system
(VM, OS, MM)
Notes: As we mentioned, program execution depends on operating system.
Different operating systems may have different ways to handle your programs.

## Slide 14
problem
electrons
algorithm
program
runtime system
(VM, OS, MM)
ISA (architecture)
Notes: Also, in hardware courses, we know that program written in high-level programming languages cannot be understood by computer hardware.
Instead, programs need to be compiled into instructions.
what instructions will your program be turned into depends on which Instruction Set Architecture (ISA) is used by your computer.
An ISA defines how to encode an instruction and how underlying hardware decodes it.

## Slide 15
problem
electrons
algorithm
program
runtime system
(VM, OS, MM)
microarchitecture
ISA (architecture)
Notes: How an instruction is processed depends on specific architecture design. For example, at any time instance, only one instruction can be executed or different instructions can be co-executed with each instruction using a different component.

## Slide 16
problem
electrons
algorithm
program
runtime system
(VM, OS, MM)
logic
microarchitecture
ISA (architecture)
Notes: Each component in use is composed by a number of digital logics,

## Slide 17
problem
electrons
algorithm
program
runtime system
(VM, OS, MM)
circuits
logic
microarchitecture
ISA (architecture)
Notes: which are constructed by integrated circuits driven by electrons.
Among all of these layers, which will be covered in computer architecture?
(levels of transformation create abstractions
Abstraction: a higher level only needs to know about the interface to the lower level,
not how the lower level is implemented)

## Slide 18: Computer Architecture!
runtime system
(VM, OS, MM)
logic
logic
microarchitecture
ISA (architecture)
problem
electrons
algorithm
program
circuits
Notes: These are the parts that will be covered in this course
Two major new parts beyond previous courses are ISA and microarchitecture;
Meanwhile, it highly couples with some background knowledge in previous courses,
Such as organization, os, and assembly language

## Slide 19: Computer Architecture!
challenging
runtime system
(VM, OS, MM)
logic
logic
microarchitecture
ISA (architecture)
Notes: So obviously it’s gonna be very challenging.

## Slide 20: Computer Architecture!
challenging
runtime system
(VM, OS, MM)
logic
logic
microarchitecture
ISA (architecture)
for me as well…
Notes: And it’s still challenging for me as well, even after years of teaching this course,

## Slide 21
for me?
Notes: Well

## Slide 22: Instructor
Kai Bu 卜凯
Associate Professor, College of CS, ZJU
Ph.D. from Hong Kong PolyU, 2013
Visiting Professor, SFU, 2018
Research Interests:
network, security, computer architecture
research interns wanted
http://list.zju.edu.cn/kaibu
Notes: I’m Kai Bu, an Associate Professor in CS college.
I graduated from Hong Kong PolyU in 2013.
I teach computer architecture.
I conduct research in networking and security.
I usually host excellent undergraduate students in my group.
If you happen to be interested in my research, I’ll be more than happy to work with you.
Before that, you might like to know more about me via my webpage.

## Slide 23: How I Prepared (and am still preparing)
read textbooks
Notes: Now back to the course, since it’s very challenging;
You might wonder that, as the instructor, how I prepared for teaching this course.
First, I read related textbooks, for many times.

## Slide 24: How I Prepared (and am still preparing)
watch video lectures
Notes: Watch online video lectures

## Slide 25: How I Prepared (and am still preparing)
practice English
Notes: Practice English

## Slide 26
and
even
read
this
book
Notes: And, I also read a book that is literally called Teaching What You Don’t Know

## Slide 27
What’s to deliver?
Notes: So, after these much preparation, what can I offer to students in my class?

## Slide 28: How a multi-core system works?
Notes: After this course, you are expected to understand how a multi-core system works;
Intro: cpu chip in this fig, multiple cores, each core has local/private L1 and L2 caches, all cores share L3 cache, connect to memory via memory controller

## Slide 29: How a multi-core system works?
Notes: Cpu and memory – computer architecture

## Slide 30: How a multi-core system works?
Notes: More examples of multi-core CPUs

## Slide 31
know not only how but also why
Notes: You’ll start paying attention to not only how something works but also why it works in that way.
You may also start wondering why it doesn’t work in some other ways.

## Slide 32
understand the principles
Notes: Through such comparison, you can better understand the working principles of things.

## Slide 33
explore the tradeoffs of
different designs and ideas
Notes: You’ll more and more get used to seeing things from different perspectives.
At most cases, a solution cannot be the best at every perspective.
You need to decide which perspective you care the most, and in order to get more benefits from this perspective, you might need to sacrifice some in terms of other perspectives.
Example, membership query using hash: space and accuracy;

## Slide 34
thought-provoking!
Notes: Probably it’ll be the most thought-provoking course you’ve even taken so far.

## Slide 35: Textbook
Computer Architecture:
A Quantitative Approach
5th edition
John L. Hennessy
David A. Patterson
Notes: The textbook we use is Computer Architecture: A quantitative approach 5th edition by Professor Hennessy and Professor Patterson.

## Slide 36: Textbook
Computer Architecture:
A Quantitative Approach
6th edition
John L. Hennessy
David A. Patterson
Notes: The content will also cover some updates from the sixth edition

## Slide 37: Online Companion
5th Edition
https://booksite.elsevier.com/9780123838728/index.php
6th Edition
https://www.elsevier.com/books-and-journals/book-companion/9780128119051
Notes: A varriety of resources are available online including reference appendices and links to related materials on the Web, etc.

## Slide 38: Why This Book?
Quantitative approach:
Performance driven
Know not only how but also why
As in this book
Operating Systems: Three Easy Pieces
Notes: So why this book?
It presents computer architecture design in a quantitative approach, which adopts a performance-driven perspective. In other words, whenever it delivers a design technique, it clearly motivates how this technique makes our computers faster or better in terms of other measurement methodology.
So it tells us not only how computer architecture works but also why it works in the way it is designed.
You are also strongly encouraged to read the book Operating Systems: Three Easy Pieces as well, as os is a prerequisite for computer architecture.

## Slide 39: Course Website
http://list.zju.edu.cn/kaibu/comparch2020/
Notes: all announcements and materials like slides and assignments will be posted on this website.

## Slide 40: Syllabus
Reference syllabus by Prof. Jiang
http://list.zju.edu.cn/kaibu/comparch2015/Syllabus_2013spring.pdf
Notes: Here’re the links for reference syllabus

## Slide 41: Schedule
Reference schedule
http://list.zju.edu.cn/kaibu/comparch2019/schedule.html
Notes: and schedule

## Slide 42: Teaching Components
Lecture
Lab OR Research
Assignment & Quiz & Exam
Notes: The course contains three major teaching components; they are lectures, labs OR research practice, and tests including assignments, quizzes, and exams;

## Slide 43: Teaching Components
Lecture
Lab OR Research
Assignment & Quiz & Exam
Notes: Let’s start from walking through the key topics to be covered in lectures.

## Slide 44: Left off in Organization
single cycle
instruction execution
Notes: This is where you left off in Computer Organization, computer hardware processes an instruction in a single clock cycle.
By single clock cycle, it means that within each clock cycle, only one instruction is being processed.
Limitation? (long clock cycles, other instructions have to wait even though some components are idle)

## Slide 45: Left off in Organization
s i n g l e c y c l e
instruction execution
Notes: This is where you left off in Computer Organization, computer hardware processes an instruction in a single clock cycle.
By single clock cycle, it means that within each clock cycle, only one instruction is being processed.
Limitation? (long clock cycles, other instructions have to wait even though some components are idle)
A long single cycle
Long single clock
Set clock frequency
To fit the longest instruction
The overall extra waiting time
For shorter instructions

## Slide 46: Left off in Organization
m u l t i p l e c y c l e s
instruction execution
Notes: This is where you left off in Computer Organization, computer hardware processes an instruction in a single clock cycle.
By single clock cycle, it means that within each clock cycle, only one instruction is being processed.
Limitation? (long clock cycles, other instructions have to wait even though some components are idle)
Or a shorter cycle, yet taking multiple cycles for an instruction (instructions with varying cycles to complete)
Discussions:
Pros and cons of multi-cycle
State diagram, diff instruction goes through different number of states
So, averagely, save extra waiting time?

## Slide 47: Now in Architecture
Pipelining
Divide instruction execution into stages

## Slide 48: Pipelining
start executing one instruction
before completing the previous one

## Slide 49: MIPS Instruction
at most 5 clock cycles per instruction
IF ID EX MEM WB

## Slide 50: MIPS Instruction
IF ID EX MEM WB
IR ← Mem[PC];
NPC ← PC + 4;

## Slide 51: MIPS Instruction
IF ID EX MEM WB
A ← Regs[rs];
B ← Regs[rt];
Imm ← sign-extended
immediate field
of IR (lower 16 bits)

## Slide 52: MIPS Instruction
IF ID EX MEM WB
ALUOutput ← A + Imm;
ALUOutput ← A func B;
ALUOutput ← A op Imm;
ALUOutput ← NPC + (Imm<<2);
Cond ← (A == 0);

## Slide 53: MIPS Instruction
IF ID EX MEM WB
LMD ← Mem[ALUOutput]; Mem[ALUOutput] ← B;
if (cond) PC ← ALUOutput;

## Slide 54: MIPS Instruction
IF ID EX MEM WB
Regs[rd] ← ALUOutput;
Regs[rt] ← ALUOutput;
Regs[rt] ← LMD;

## Slide 55: Structural Hazard
Example
1 mem port
mem conflict
data access
vs
instr fetch
Load
Instr i+3
Instr i+2
Instr i+1
MEM
IF
Notes: Here’s an example of structural hazard due to memory conflict.
Assume the processor has only memory port.
A structural hazard will arise in clock cycle 4 when the load instruction reads data from memory and instruction i plus 3 fetches instruction from memory.

## Slide 56: Data Hazard
DADD
DSUB
AND
OR
XOR
R1, R2, R3
R4, R1, R5
R6, R1, R7
R8, R1, R9
R10, R1, R11
R1
No hazard
1st half cycle: w
2nd half cycle: r
Notes: In this example, the subtract and AND instructions need R1 before the add instruction prepares it. So R1 causes a data hazard that prevents normal pipelining of the subtract and AND instructions.
Note that the OR instruction has no hazard because the add instruction prepares R1 in the first half of the clock cycle while the OR instruction needs R1 till the second half.

## Slide 57: Memory Hierarchy

## Slide 58: Cache Performance
Memory stall cycles
the number of cycles during processor is stalled waiting for a mem access
Miss rate
number of misses over number of accesses
Miss penalty
the cost per miss (number of extra clock cycles to wait)

## Slide 59: Block Placement

## Slide 60: Multilevel Cache
Two-level cache
Add another level of cache between the original cache and memory
L1: small enough to match the clock cycle time of the fast processor;
L2: large enough to capture many accesses that would go to main memory, lessening miss penalty

## Slide 61: Virtual Memory
Program uses
discontiguous memory locations
Use secondary/non-memory storage

## Slide 62: Virtual Memory
Program thinks
contiguous memory locations
larger physical memory

## Slide 63: Prior Virtual Memory
allocated
allocated
Process A
Process B
Main/Physical Memory
Contiguous allocation
Direct memory access
Direct memory access
Notes: If we directly map process address space to physical memory address, we need to follow contiguous allocation like this.
Then each process can use direct memory access using physical memory address.

## Slide 64: Prior Virtual Memory
efficiency?
Process A
Process B
Main/Physical Memory
used
used
Notes: One possible limitation of such direct memory access is low memory efficiency.
As we can see, at certain time instants, a process uses way less memory than it is allocated for.

## Slide 65: Prior Virtual Memory
protection?
Process A
Process B
Main/Physical Memory
used
used
Notes: Another limitation is lack of memory protection to prevent a process from accessing memory allocated for other processes.

## Slide 66: Prior Virtual Memory
Process A
Process B
Main/Physical Memory
used
used
Virtual memory
used
used
Easier/flexible memory management
Notes: To address the above limitations, virtual memory introduces an indirect mapping from the memory address processes use to the physical memory address where data actually locates.

## Slide 67: Prior Virtual Memory
Process A
Process B
Main/Physical Memory
used
used
Virtual memory
used
used
Share a smaller amount of physical memory among many processes
Notes: Each process still thinks that the same amount of memory space is allocated for it;
But in practical, not all data need to be pre-loaded into memory and processed data could be evicted from memory.
This way, a smaller physical memory can support more processes.

## Slide 68: Prior Virtual Memory
Physical memory allocations
need not be contiguous
Process A
Process B
Main/Physical Memory
used
used
Virtual memory
used
used
used
used
used
used
Notes: Besides, memory allocations no longer need to be contiguous,
Virtual address can point to any physical address.

## Slide 69: Prior Virtual Memory
memory protection;
process isolation
Process A
Process B
Main/Physical Memory
used
used
Virtual memory
used
used
used
used
used
used
Notes: As now processes access memory through virtual address instead of physical address,
with well designed address mapping,
we can make sure that a process cannot access memory allocated for other processes.

## Slide 70: Prior Virtual Memory
Process A
Process B
Main/Physical Memory
used
used
Virtual memory
used
used
used
used
used
used
Introduces another level of
secondary storage
Notes: To support larger virtual memory space, data blocks corresponding to virtual addresses can also be temporarily stored in secondary storage like disk and swapped to memory when needed.

## Slide 71: Virtual Memory
Paged virtual memory
page: fixed-size block
Segmented virtual memory
segment: variable-size block

## Slide 72: Virtual Memory
Paged virtual memory
page address: page # + offset
Segmented virtual memory
segment address: seg # + offset

## Slide 73: TLB Example
Opteron data TLB
Steps 1&2: send the virtual address to all tags
Step 2: check the type of mem access against protection info in TLB
https://www.youtube.com/watch?v=95QpHJX55bM
Notes: Here’s an example of how TLB works for address translation.
First, the virtual page number is sent to compare with all tags;

## Slide 74: TLB Example
Opteron data TLB
Steps 3: the matching tag sends phy addr through multiplexor
Notes: The matching tag returns its physical page number through multiplexor;

## Slide 75: TLB Example
Opteron data TLB
Steps 4: concatenate page offset to phy page frame to form final phy addr
Notes: Then the physical page number is combined with page offset to form the physical address.

## Slide 76: Virtual Memory + Caches

## Slide 77: Disk
http://www.cs.uic.edu/~jbell/CourseNotes/OperatingSystems/images/Chapter10/10_01_DiskMechanism.jpg

## Slide 78: Disk Arrays
Disk arrays with redundant disks to tolerate faults
If a single disk fails, the lost information is reconstructed from redundant information
Striping: simply spreading data over multiple disks
RAID: redundant array of inexpensive/independent disks

## Slide 79: RAID

## Slide 80: RAID 0
JBOD: just a bunch of disks
No redundancy
No failure tolerated
Measuring stick for other RAID levels: cost, performance, and dependability

## Slide 81: RAID 1
Mirroring or Shadowing
Two copies for every piece of data
one logical write = two physical writes
100% capacity/space
overhead
http://www.petemarovichimages.com/wp-content/uploads/2013/11/RAID1.jpg

## Slide 82
https://www.icc-usa.com/content/raid-calculator/raid-0-1.png

## Slide 83: RAID 2
http://www.acnc.com/raidedu/2
Each bit of data word is written to a data disk drive
Each data word has its (Hamming Code) ECC word recorded on the ECC disks
On read, the ECC code verifies correct data or corrects single disks errors
Notes: Each bit of data word is written to a data disk drive, accompanied with the word’s ECC spread over the ECC disks

## Slide 84: RAID 3
http://www.acnc.com/raidedu/3
Data striped over all data disks
Parity of a stripe to parity disk
Require at least 3 disks to implement

## Slide 85: RAID 3
P
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
Even Parity
parity bit makes
the # of 1 even
p = sum(data1) mod 2

## Slide 86: RAID 3
Even Parity
parity bit makes
the # of 1 even
p = sum(data1) mod 2
Recovery
if a disk fails,
“subtract” good data
from good blocks;
what remains is missing data;
P
1
0
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1

## Slide 87: RAID 3
Even Parity
parity bit makes
the # of 1 even
p = sum(data1) mod 2
Recovery
if a disk fails,
“subtract” good data
from p of good blocks;
what remains is missing data;
P
1
0
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
1
0
0
1
1
0
1
“subtract”
1 – 1 = 0
1 – 0 = 1
0 – 1 = 1
0 – 0 = 0

## Slide 88: RAID 4
http://www.acnc.com/raidedu/4
Favor small accesses
Allows each disk to perform independent reads, using sectors’ own error checking
independent read - not read across multiple disks

## Slide 89: RAID 3 & RAID 4
bottleneck:
single parity disk
access:
parallel vs independent

## Slide 90: RAID 3 & RAID 4
? bottleneck:
single parity disk
access:
parallel vs independent

## Slide 91: RAID 5
http://www.acnc.com/raidedu/5
Distributes the parity info across all disks in the array
Removes the bottleneck of a single parity disk as RAID 3 and RAID 4

## Slide 92: RAID 6: Row-diagonal Parity
RAID-DP
Recover from two failures
xor⊕
row: 00⊕11⊕22⊕33=r4
diagonal: 01⊕11⊕31⊕r1=d1

## Slide 93: RAID 6: Row-diagonal Parity
RAID-DP
Recover from two failures
xor⊕
row: 00⊕11⊕22⊕33=r4
diagonal: 01⊕11⊕31⊕r1=d1

## Slide 94: Double-Failure Recovery

## Slide 95: Double-Failure Recovery

## Slide 96: Double-Failure Recovery

## Slide 97: Double-Failure Recovery

## Slide 98: Double-Failure Recovery

## Slide 99: Double-Failure Recovery

## Slide 100: Double-Failure Recovery

## Slide 101: Double-Failure Recovery

## Slide 102: Double-Failure Recovery

## Slide 103: Double-Failure Recovery

## Slide 104: Double-Failure Recovery

## Slide 105: Double-Failure Recovery

## Slide 106: Double-Failure Recovery

## Slide 107: centralized shared-memory
eight or fewer cores

## Slide 108: centralized shared-memory
Share a single centralized memory
All processors have equal access to

## Slide 109: centralized shared-memory
All processors have uniform latency from memory
Uniform memory access (UMA) multiprocessors

## Slide 110: distributed shared memory
more processors
physically distributed memory

## Slide 111: distributed shared memory
more processors
Distributing mem among the nodes
increases bandwidth & reduces local-mem latency
physically distributed memory

## Slide 112: distributed shared memory
more processors
NUMA: nonuniform memory access
access time depends on data word loc in mem
physically distributed memory

## Slide 113: distributed shared memory
more processors
Disadvantages:
more complex inter-processor communication
more complex software to handle distributed mem
physically distributed memory

## Slide 114: Cache Coherence Problem
A memory system is Coherent if any read of a data item returns the most recently written value of that data item
Two critical aspects
coherence: defines what values can be returned by a read
consistency: determines when a written value will be returned by a read

## Slide 115: Cache Coherence Problem
write-through cache
w/o precautions
Notes: The problem concerning whether the value of shared data is identical in different caches is called cache coherence problem.

## Slide 116: Textbook Navigation
Fundamentals: Chapter 1
Instruction: Appendix C & Chapter 3
Memory: Appendix B & Chapter 2
Storage: Appdenix D
Multiprocessor: Chapter 5

## Slide 117: Teaching Components
Lecture
Lab OR Research
Assignment & Quiz & Exam
Notes: Together with lecture sessions, we also have tight lab schedules to practice what we learn.

## Slide 118: Labs
6 lab sessions (tentative)
Pipeline implementation
Cache implementation
Demo: individual OR group of up two
Report: individual
Notes: In particular, through 6 lab assignments, we aim to implement pipeline and cache.

## Slide 119: Labs
Lab 1
warmup Spartan 3E and ISE environment;
update verilog code of multi-cycle CPU to 3E board;
add one new branch instruction;
reference code:
Spartan 3E Display: http://list.zju.edu.cn/kaibu/comparch/lab1-Spartan3E-Display.rar
Spartan Simulation: http://list.zju.edu.cn/kaibu/comparch/spartansimulation.txt
Notes: In the first lab session, we start from warming up the experiment environment.
Here are some reference codes you might use to get experiment tools work.

## Slide 120: Labs
Lab 2
implement 5-stage pipelined CPU with 15 MIPS instructions;
Lab 3
implement stall technique against pipelining hazards;
Lab 4
implement forwarding paths toward faster CPU;
Lab 5
implement a pipelined CPU with 31 MIPS instructions;
use predict-not-taken policy to solve control hazard;
Lab 6
cache (tbd)
Notes: Labs 2 through 5 are dedicated to pipeline implementation while lab 6 is for cache implementation.

## Slide 121: Labs
Call for lab assistants
help tutor & check the demo during lab sessions;
get bonus credit;
Notes: For students who are familiar with lab experiments, you are strongly encouraged to join me as lab assistants.
As a lab assistant, you are expected to help tutor students and check demos.
Then, of course, you can get bonus credit as reward.

## Slide 122: Teaching Components
Lecture
Lab OR Research
Assignment & Quiz & Exam
Notes: Together with lecture sessions, we also have tight lab schedules to practice what we learn.

## Slide 123: Research Practice
http://list.zju.edu.cn/kaibu/comparch2020/
research.html
WOW THE CLASS!

## Slide 124
Why do you care?
Notes: So why do u care about the research part?

## Slide 125
waive lab demos&reports
Notes: So why do u care about the research part?

## Slide 126
spice up
graduate application

## Slide 127: Special Thanks
Weixin Liang (Stanford)
Ke Li (Columbia)
Jinhong Li (CUHK)
Min Huang (CMU)
Qinhan Tan (Princeton)
Zhihua Zeng (VMware)
Yiming Wei (ZJU)
Chenlu Miao, Jingsen Zhu, Miao Zhang, Xingjian Zhang, Yuan Tian, Tianqi Song

## Slide 128: WOW
PhantomCache
NDSS 2020
MemCloak
ACSAC 2018

## Slide 129
More than that?
Notes: But what’s more than that is if you really go deep into the research practice,

## Slide 130
learn to learn things differently
Notes: You’ll learn to learn things differently

## Slide 131
know not only how but also why
Notes: You’ll start paying attention to not only how something works but also why it works in that way.
You may also start wondering why it doesn’t work in some other ways.

## Slide 132
read this book and you’ll see Operating Systems: Three Easy Pieces http://pages.cs.wisc.edu/~remzi/OSTEP/
Notes: Again, I’m recommending the book Operating Systems: three easy pieces;
It’ll help to shape your research mind as well as build background knowledge for computer architecture.

## Slide 133
Grade?
Notes: Finally, the part you care the most,

## Slide 134: Grading (tentative)
4% | Class Participation & Performance
16% | Assignment
8% | Quiz
32% | Lab OR Research
40% | Final Exam closed-book + memo 10:30 – 12:30, January 23, 2021
Notes: Grading policy
Now we’ve talked about several components this course requires, here’s how they contribute to the final grade.

## Slide 135: How will I teach?
Notes: Then, how will I teach?

## Slide 136: What Students Expect from Teachers
Fun
Humor
Expertise
Easy exam
High grades
…
Notes: For most of us, an ideal teacher should be fun and humorous, meanwhile, he or she should be an expert for what is taught.
More important, exams should be easy and grades should be high.

## Slide 137: I wish I knew someone like this, too…
Notes: Well, you can’t always get what u want, right?

## Slide 138: Teaching Plan
Keep it Simple
Focus on the core concepts
Try to help you more easily understand
Notes: So here’s how I teach.
As a junior faculty member, I’m gradually getting familiar with what I teach as well.
For every teaching component, I’ll try to keep it simple and focus on the core concepts. The ultimate goal of my teaching is to help you more easily understand what the textbook delivers.

## Slide 139: Learn, Teach, Inspire
Teach to Learn: A Privilege of Junior Faculty
“If we can contribute, in whatever way,
to a students' pursuit of a better self,
even if it is not about the course per se,
we still succeed as educators.”

## Slide 140: Rumor Has It?
find out more from
Q11.pdf

## Slide 141: To Every One of A Kind
find out more from
Q11.pdf 2nd edition
Notes: Also value students’ goals and strengths, and try to help them if possible…;

## Slide 142
#What’s More to Share
helpful/inspiring resources
#The 3 Secrets of Highly Successful Graduates by Reid Hoffman
Notes: I’ll also share with you some helpful or inspiring videos and articles.

## Slide 143
How will you contribute?
Notes: Besides my efforts, your contributions are also indispensible.

## Slide 144: Thanks In Advance
Study group
Lab assistants
Research interns
…
AT LEAST
submit assignments & lab reports
show up to final exam
Notes: For example, you can start study groups for peer discussion, you can help me as lab assistants or research interns.
At least, please submit assignments in time and show up to final exam.
Believe it or not, some students just don’t.

## Slide 145
Enjoy, xixi
Notes: Hope you’ll enjoy

## Slide 146
Deal?

## Slide 147
QQ Group: 533944879
Notes: One more request, join this qq group for ease of off-line discussion.

## Slide 148
WOW, Member #400

## Slide 149: ?
Notes: So far, we have introduced course logistics and contents.
Any questions?

## Slide 150: Who’s Who
Notes: Roster;
Now it’s time for the class to get the first impression of each of you.
Briefly introduce yourself if you like when I call ur name; you could use either English or Chinese.

## Slide 151: Ready?
Notes: Great to know u all,
Now, Ready for an adventure to computer architecture?

## Slide 152
#The 3 Secrets of Highly Successful Graduates
Notes: Cause if not now, when?